Hello, my name is Sharon Nichols and I work at Texas School for the Blind and Visually Impaired. This video will be a physical description of a Braille Sense U2 with a braille type keyboard.

(Pause)

On the top of the Braille Sense is a Perkins-style keyboard, with a "SPACEBAR", "BACKSPACE", and "ENTER" key.

(Pause)

On the same row as the Space bar are 4 rectangular keys,

(Pause)

two on the left of the spacebar, and two on the right.

(Pause)

Moving from left to right, the key to the far left is the "F1" key, and the next  is the "F2" key.

(Pause)

The key to the right of the spacebar is the "F3" key, and then "F4" key.

(Pause)

We will explore the function keys in a later video.

(Pause)

Below the keyboard is a 32 cell Braille display.

(Pause)

Above the Braille display, there are 32 small, oval-shaped buttons

(Pause)

These buttons are called cursor routing keys. When you are editing documents, you can use these keys to move your cursor, much like clicking a mouse.

(Pause)

On each side of the Braille display are two capsule shaped keys. These are the "UP" and "DOWN" scroll keys.

(Pause)

The scroll keys are used to scroll the Braille display through text, menus or lists.

(Pause)

Near the top center of the panel, is an LCD display.

(Pause)

The LCD display allows the teacher or anyone helping the student to see what is shown on the Braille Sense, such as menus or text.

(Pause)

Stereo speakers are located on each side of the LCD for audio output.

(Pause)

To the right of the LCD, along the top edge of the unit, there are 4 LED lights.

(Pause)

The far left LED light shows wireless status; when the wireless is on, this LED light turns blue.

(Pause)

The next LED indicates Bluetooth status; again, when Bluetooth is on, this LED light turns blue.

(Pause)

The third LED light shows the status of the GPS receiver; when you are running Sense Navigation, the LED turns blue (this is an add on software feature you have to purchase).

(Pause)

The LED light on the far right indicates power status. When the Braille Sense U2 is on, the LED turns red.

(Pause)

These LED lights help a teacher easily see what the student is using to complete their work. Sometimes it will allow the teacher to know when to tell the student to turn off the WIFI when it is not necessary.

(Pause)

### Now we will look at the right side panel

(Pause)

There is a section with 2 ports.

(Pause)

The port nearest the front of the unit is a mini USB port. You can connect your Braille Sense to a computer using this USB port, and use it as a Braille terminal for the computer.

(Pause)

Behind the USB port is the jack to charge the battery or use it on AC power.

(PauseP

Near the rear of the right panel is a 3-position slide switch. This is the key "Lock" switch. I'll explain this later.

(Pause)

Now let's look at the left panel

### (Pause)

Near the front of the unit are 2 full-sized USB ports. You can use these ports to connect a USB drive, a USB keyboard or printer.

(Pause)

Near the back on this side is the SD card slot, Which can be used like a USB drive.

(Pause)

### Now let's look at the back panel

(Pause)

On the far left is a small, round recess, with a dot-like button inside it. This is the "RESET" button. If your unit is not responding properly, you can press this button to force a reboot of the braille sense. It takes about fifteen seconds to reboot.

(Pause)

To the right of the "RESET" button, is the LAN port. This allows you a wired connect to the Internet. Much like you use for your computer at school.

(Pause)

To the right of the LAN port is another USB port.

(Pause)

Next is a video output (VGA) port to connect to a computer display. This feature is very helpful since it allows the teacher to see the student's work.

(Pause)

On the far right of the back panel, is the detachable battery.

(Pause)

### Finally let me show you the front panel

(Pause)

On the far left is an emblem displaying the location of the GPS antenna.

(Pause)

To the right of the "GPS" emblem, is the stereo microphone jack, used for connecting an external microphone.

(Pause)

To the right of the microphone jack is the stereo headphone jack.

(Pause)

To the right of the headphone jack is another 3-position slide switch. This is the "Media Mode" switch, which I will discuss later.

(Pause)

To the right of the "Media Mode" switch, are five buttons. The buttons control media playback, DAISY playback, or the FM radio.

(Pause)

To the right of the media buttons is the on/off switch. To turn it on, push the switch to the right. To turn it off, push it to the right again. You will hear it tell you if the power is on.

(Pause)

OK, that describes and shows you the physical parts of the Braille Sense U2, in the next video I will show you how to navigate the Menu system.